## Slide 1: výukový materiál Flight Plan AJ.01.01.19
Autor: Milan Junášek
Projekt: Modernizace výuky pomocí ICT CZ.1.07/1.5.00/34.1057

## Slide 2: Basics of Aviation English
Unit 10: Flight Plan
<footer>

## Slide 3: Unit 10: Flight Plan
Flight plans are documents filed by pilots to the local civil aviation authority before departure. They contain basic information as point of departure and arrival, alternate airports, pilot´s information, type of flight, number of passengers, aircraft technical data etc. Some may think its useless paperwork. However, careful flight planning can not only save flying costs, but even save lifes if some emergency situation occurs.

## Slide 4
Task 1: Study the International Flight Plan form in your
task sheet. Discuss the meaning of each box, then see
the explanations and examples here.
Unit 10: Flight Plan
Note: You don´t have to care too much about the first part of the form as it contains only address of the aviation authority, person who created the flight plan and time of filing.

## Slide 5: Unit 10: Flight Plan
Aircraft registration letters and numbers or operating agency and flight number, callsign
Flight rules, usually V for VFR flight, I for IFR flight, but there are also some other options
options: S for scheduled, N for non scheduled, G for general aviation, M for military
B A W 7 4 W
I
S

## Slide 6: Unit 10: Flight Plan
Specification of number of aircraft in case of a group, othewise left blank
2 to 4 characters, international code of the aircraft type, for example C172 for Cessna 172
depending on maximum certificated takeoff mass. L (light) for less than 7000kg, M (medium) for 7000-136000 and H (heavy) for more
B 7 3 7
M

## Slide 7: Unit 10: Flight Plan
List of communication, navigation and surveillance equipment on board (COM/NAV/SSR). There are many options, but very often letter S is used for standard equipment consisting of VHF RTF, VOR and ILS. A letter for transponder type is used after the stroke (/).
ICAO aerodrome designator of departure airport
departure time
S C
E G L L
0 8 3 0

## Slide 8: Unit 10: Flight Plan
True airspeed during cruise part of the flight. A letter specifies units used, K for kilometres per hour, N for knots.
Planned cruising level. Letter F used for Flight level, A for altitude in hundreds of feet. For uncontrolled VFR flight, just the letters VFR are filled in.
Description of planned flight route (not necessary for some GA flights). Using points, routes or their segments, standard departure or arrival routes (SIDs and STARs) etc.
K 0 2 5 0
F 2 2 0
EGLL BPK M185 CLN UL620 BESIP L620 LISBA T620 GOLOP LKPR

## Slide 9: Unit 10: Flight Plan
ICAO aerodrome designator of the destination airport
Total Estimated Elapsed time for the flight
Other additional, important or helpful information
L K P R
ICAO aerodrome designator of the alternate airport
L K T B
0 2 4 0

## Slide 10: Unit 10: Flight Plan
The fuel endurance for the flight
Number of persons on board
There are many more more rules and options for filling a flight plan. You can find more information on the Internet, you can try for example this website:
http://www.skybrary.aero/index.php/Flight_Plan_Filling
0 4 0 0
1 1 5

## Slide 11: Unit 10: Flight Plan
Task 2: Look at information about a planned flight in
your worksheet and try to transfer it in the flight plan.
You can use the form from Task 1 and fill it in according
to this information

## Slide 12: Unit 10: Flight Plan
This is the end of the lesson and also of the course.
I hope you have enjoyed it and you will find some of the information useful in future – maybe when you prepare for becoming a pilot…
Goodbye and Have a nice flight!

## Slide 13: Unit 10: Flight Plan
Used pictures:
Sunset. russavia. [cit. 2013-06-25]. Dostupný pod licencí Creative Commons na WWW: http://en.wikipedia.org/wiki/File:Last_Glimpse_of_Sunset_%282885821239%29.jpg
Icao flight plan. ICAO. [cit. 2013-06-25]. Dostupný pod licencí Creative Commons na WWW: http://en.wikipedia.org/wiki/File:Icao_flight_plan.jpg

## Slide 14
Credits:
Presentation background: Milan Junášek
Aviation information resources:
www.wikipedia.org www.icao.int
www.flightsim.cz
www.ivao.cz
www.lis.rlp.cz
Verification:
Střední škola letecké a výpočetní techniky, Odolena Voda, www.sslvt.cz
Milan Junášek 2013